## Slide 1: RTKLIB Tools Supporting Aceinna Format
2021-01-05

## Slide 2: Content
what is rtklib
rtklib tools supporting Aceinna Format
aceinna data format
use strsvr to decode aceinna-user data
use rtknavi to decode aceinna-user data
use rtknavi to decode aceinna-raw data
use rtknavi to save ins2000 data and decode

## Slide 3: What is rtklib
rtklib is an open-source program package for standard and precise positioning with GNSS (global navigation satellite system). It supports standard and precise positioning algorithms with GPS, GLONASS, Galileo, QZSS, BeiDou and SBAS.

## Slide 4: Rtklib tools supporting Aceinna Format
rtklib tools supporting aceinna format is a special version of rtklib which supports aceinna data format to display data, decode data, save data and also plotting and RTK processing.
rtklib with Aceinna format binary version:
https://github.com/Aceinna/rtklib_bin_aceinna
rtklib with Aceinna format source version:
https://github.com/Aceinna/rtklib_aceinna
A special OpenRTK330LI firmware “OpenRTK330L-GNSS_RTK_INS_NEW_DATA_FORMAT.bin”supports
new aceinna data format output. The download links is as follow
https://developers.aceinna.com/code/apps

## Slide 5: Aceinna data format
Aceinna-user and aceinna-raw are two data formats exported from Openrtk330LI. The data is outputted from serial port 1 and serial port 3 of Openrtk330LI. Aceinna-user data includes imu raw data, rtk and ins solution; Aceinna-raw includes rover, base RTCM data and imu raw data.

## Slide 6: Aceinna-user format
Data format definition
Description
Start: Each frame of data starts with this, 2 bytes: 0x55 0x55.
Frame type: 2 bytes, high byte first.
Data length: 1 byte, refers to the byte length of the data content.
Data content: maximum 255 bytes.
Check: crc16 check, 2 bytes, low byte first, bytes from the beginning of the “Frame type” to the end of the “Data content” are included in the check calculation, and the check algorithm C code is as follows:
Start 1 | Start 2 | Frame type 1 | Frame type 2 | Data length 1 | Data content | Check 1 | Check 2

## Slide 7: Aceinna-user format
uint16_t CalculateCRC (uint8_t *buf, uint16_t length)
{
uint16_t crc = 0x1D0F;
for (int i=0; i < length; i++) {
crc ^= buf[i] << 8;
for (int j=0; j<8; j++) {
if (crc & 0x8000) {
crc = (crc << 1) ^ 0x1021;
}
else {
crc = crc << 1;
}
}
}
return ((crc << 8 ) & 0xFF00) | ((crc >> 8) & 0xFF);
}

## Slide 8: Aceinna-user format
Frame types
Aceinna-user has five types of data, namely "S1", "G1", "I1", "O1" and "Y1"; For the specific structure of each type of format, please refer to the openrtk documentation：
https://openrtk.readthedocs.io/en/latest/communication_port/User_uart.html#imu-raw-data-packet

## Slide 9: Aceinna-raw format
Aceianna-raw is composed of four format types of $GPGGA，$GPIMU，$GPROV，$GPREF.
$GPGGA
$GPGGA is the standard NMEA GGA format.
$GPIMU
$ GPIMU is the IMU information in NMEA format.
$GPIMU | time of week | accel-x | accel-y | accel-z | gyro-x | gyro-y | gyro-z

## Slide 10: Aceinna-raw format
$GPROV
$ GPROV contains the RTCM package from Rover.
$GPBAS
$GPBAS contains the RTCM package from Base.
$ GPROV | time of week | left length | RTCM bin | 
$ GPBAS | time of week | left length | RTCM bin | 

## Slide 11: Use strsvr to decode aceinna-user data
Use strsvr to decode aceinna-user data format. Decode aceinna format data and display information in monitor dialog and save it in files.
Select serial for (0) input. Click “opt” button to open the Serial Options dialog.

## Slide 12: Set input stream parameter
Bitrate is selected as 460800.

## Slide 13: Set output files path
Select the path to save the file. For example: C:\Users\zhangchen\Desktop\rtklog\.

## Slide 14: Show the data in monitor dialog and save file
Click the small square button to open Input Stream Monitor dialog.

## Slide 15: Show the data in monitor dialog and save file
Select the aceinna-user format.

## Slide 16: Show the data in monitor dialog and save file
Click “start” button to start receiving data.

## Slide 17: Show the data in monitor dialog and save file
Strsvr is running, the data decoding information is showed in monitor dialog. The file is saved in the previous output path

## Slide 18: Use RTKLIBNAVI to decode aceinna-user data
Aceinna-raw data is the result output from openrtk330. Using rtklibnavi to connect the first serial port of openrtk330, the RTK processing result data can be recognized. These data can be displayed by SNR plot, sky map and GND Trk.
SNR plot, star map and GND Trk

## Slide 19: Set input stream parameter
Click the ‘I’ button to open Input Streams dialog.
Check (1) Rover in the Input Streams dialog.

## Slide 20: Set input stream parameter
Select “serial” in the type option.
Click the opt button to open the Serial Options dialog.

## Slide 21: Set input stream parameter
Select the first serial port in the serial Options dialog.

## Slide 22: Set input stream parameter
Bitrate is selected as 460800.

## Slide 23: Set input stream parameter
Format is selected as Aceinna-user.

## Slide 24: Set output log files path
Click the ‘L’ button to open Log Streams dialog.

## Slide 25: Set output log files path
Check (6)Rover ,select File type and input the log file paths. Click OK button.

## Slide 26: Start to receive data
Click the start button to start receiving the data.

## Slide 27: Start to receive data
When receiving the data, the SNR bar is plotted. Click the arrow button to switch view (SNR bar, sky map, positioning coordinates, horizontal error scatter, position error timeseries in north, east and up).

## Slide 28: Start to receive data
The sky map.

## Slide 29: Start to receive data
Both sky map and SNR plot.

## Slide 30: Start to receive data
The Gnd Trk.

## Slide 31: Start to receive data
Click the Plot button to open RTKPLOT.

## Slide 32: Start to receive data
The RTKPLOT dialog. Select the drop-down list to switch views. The Position error time series are plotted.

## Slide 33: Start to receive data
Click Stop button to stop receiving data. The output file is saved in the selected output path.

## Slide 34: Use RTKLIBNAVI to decode aceinna-raw data
Aceinna-raw data contains the original data of rover station and base station. Using rtklibnavi to connect the third serial port of openrtk330, the rover station and the base station information can be read at the same time. These data can be displayed by SNR plot, sky map, baseline and GND Trk. At the same time, these data can also be used for RTK processing.

## Slide 35: Use RTKLIBNAVI to decode aceinna-raw data
SNR plot, star map, baseline and GND Trk

## Slide 36: Set input stream parameter
Click the ‘I’ button to open Input Streams dialog.

## Slide 37: Set input stream parameter
Check (1) Rover in the Input Streams dialog.

## Slide 38: Set input stream parameter
Select serial in the type option.

## Slide 39: Set input stream parameter
Click the opt button to open the Serial Options dialog.

## Slide 40: Set input stream parameter
Select the third serial port in the serial Options dialog.

## Slide 41: Set input stream parameter
Bitrate is selected as 460800.

## Slide 42: Set input stream parameter
Format is selected Aceinna-raw.

## Slide 43: RTK processing config
Close the Input Streams dialog and click the options button to open the options dialog.

## Slide 44: RTK processing config
In the options dialog, choose the RTK posting mode option as “kinematic” or “static”.

## Slide 45: Start to receive data
Click the start button to start receiving the data.

## Slide 46: Start to receive data
When receiving the data, the SNR map of Rover and base according to the data will appear in GUI, and RTK results will be displayed.

## Slide 47: Start to receive data
Click the arrow button to switch view(SNR bar, sky map, positioning coordinates, baseline, horizontal error scatter, position error timeseries in north, east and up).

## Slide 48: Start to receive data
The sky maps.

## Slide 49: Start to receive data
The baseline.

## Slide 50: Start to receive data
The Gnd Trk.

## Slide 51: Start to receive data
Click the Plot button to Open RTKPLOT.

## Slide 52: Start to receive data
The RTKPLOT dialog.

## Slide 53: Start to receive data
Select the drop-down list to switch views.

## Slide 54: Start to receive data
The position error time series views.

## Slide 55: Use RTKLIBNAVI to decode INS2000 data and decode
Click the [i] button in the upper right corner to open the [input streams] dialog box.

## Slide 56
Check [(1) Rover], select [serial] for [type], select [ins2000] for [format], and click [Opt] to open the [serial options] dialog box.

## Slide 57
[port] select the serial port of ins2000, and [bitrate] select 460800. Click [OK] to close the dialog box.

## Slide 58
Click the [l] button in the upper right corner to open the [log streams] dialog box.

## Slide 59
Check [(6) Rover], [type] select [file], and then select a path to save the file, and click [OK] to close the dialog box.

## Slide 60
Click [start] to start data collection and decoding.